## Slide 1: Battery

## Slide 2: Battery Agenda
Back ground information
Lithium cell Model creation
Data Collection
Parameter estimation
Battery pack model creation

## Slide 3: Battery Function
The battery has two main functions within this electrical circuit:
Guarantee a minimal autonomy according to the testing requirements
Act as a buffer to supply power when the power sources are unable to meet the demand from the motors and to level current peaks

## Slide 4: Types of batteries
Batteries in general can be classified into two main categories:
1- Primary (non-rechargeable)
Such as: Zinc-Carbon battery, Alkaline battery and Lithium battery.
2- Secondary (rechargeable)
Such as: Lead acid, Lithium Ion, Nickel Cadmium and Nickel Metal Hydride.
Unlike car battery, deep cycle batteries that are used in renewable energy applications are meant to be discharged and recharged (cycled) repeatedly.

## Slide 5: Deep Cycle Battery
Solar Batteries (Deep Cycle Batteries) are a key component in a stand-alone renewable energy system. As they accumulate excess energy created by your system and store it to be used when there is no other energy input.
Installing solar panel system tied to utility grid, will still need deep cycle batteries in case of using power in the event of an outage. Without deep cycle batteries, you can only use power at the time you produce it (i.e. you will not have power when the sun isn't out if you don't have batteries in your solar electric system).

## Slide 6: Deep cycle battery

## Slide 7: Battery Descriptions
1)Rated Voltage: 12v , 24v and 48v
2)Rated Capacity: 1,2,3,10.. Ah
3) Cycle Lifetime of the battery:
the ability of the battery to charge and discharge till 80% of the nominal capacity.

## Slide 8
4) State of Charge (SOC) and Depth of Discharge (DOD):
they both are complementary to each other but SOC is normally used when discussing the current state of a battery in use, while DOD is most often seen when discussing the lifetime of the battery after repeated use.
5) “C” rate :
C-rate is the current which we use how fast the cell is charging or discharging.
1C means to allow the cell to charge/discharge in 1 hour. 0.5C means to allow the cell to charge/discharge in 2 hour. 2C mean half hour and so on.

## Slide 9: What does DOD effect?

## Slide 10: Series and parallel batteries
1-series:
2-Parallel

## Slide 11: Equivalent-Circuit Cell Modeling

## Slide 12: I- open circuit voltage

## Slide 13: 2- terminal voltage

## Slide 14: 3-Transient dynamics

## Slide 15: Neglect parasitic loses

## Slide 16: Steps of creating a battery cell model

## Slide 18: Battery model in Math lab

## Slide 19: Thermo model for heat generation

## Slide 21: Pulse charge and discharge technique

## Slide 22: The signal pulsar scoop

## Slide 23: What is data required
Relevant operation condition ranges of:
Temp
SOC
Current
Measured Data:
Constant current discharge
Pulse discharge
Pulse charge

## Slide 24: Constant current

## Slide 25: Function of the signal pulsar

## Slide 26: What is the transient dynamics